IP Networks Lab Work 1 Report
       Khaliq Aghakarimov
1. Your workstation
3. hostname=user-Veriton-X2640G. The same as in your terminal <username@hostname>
4. No domain: null

2. Addresses of your workstation
1. MAC address (or ethernet number): f4:4d:30:9e:2e:f1
2. IP address (or inet address): 192.168.34.52
Mask: 255.255.252.0, so 22 bits for the subnet mask
3. in CIDR notation: 192.168.34.52/22
4.
    11000000 10101000 00100010 00010110
AND
    11111111 11111111 11111100 00000000
We get

11000000 10101000 00100000 00000000 = 192.168.32.0 (Network IP address).
5. There are 10 bits that are 0 in the subnet mask. So 2^10 = 1024 hosts. Then
192.168.32.1 – 192.168.32.255
192.168.33.0 – 192.168.33.255
192.168.34.0 – 192.168.34.255
192.168.35.0 – 192.168.35.254
~1024 hosts according to the IP addresses above. So 192.168.35.255 is the broadcast address.
Broadcast address in
decimal notation: 192.168.35.255
binary notation: 11000000 10101000 00100011 11111111

6. 2^10-2 = 1022 IP numbers are available which means this much different machines can be connected.

7. From settings one can find that the IP address of default router is 192.168.35.254 (in my case).
8. Loopback (lo): inet address=127.0.0.1
9. That is your own local machine who answers to the command <ping 127.65.43.21>.
10. 11111111 00000000 00000000 00000000 (A network class)
2^24-2 IP numbers which means my machine has this much IP numbers that can be used for	loopback.

3. Using the ping command
1. Typing <ping your IP address> ICMP requests will be sent to local hosts. One also gets the number of bytes and packets transmitted or received, for each packet there’s a certain time for transmission + coming back.
2. There are some options that could be useful while using ping command:
-i: to increase/decrease time interval between 2 consecutive pings
-s: or changing packet size
-c: set ping to send a concrete number of packets
-w: set ping timeout, etc.

4. Other workstations
1. Type “host www.ufaz.az”. One can get 128.199.45.141 which is the IP number of the University web server.
2. Type “host moodle.unistra.fr”. One can get 130.79.225.12 which is the IP number of moodle server.
3. wiki-litis.insa-rouen.fr is the name of the machine whose IP number is 194.254.17.24.
4. Type “host www.insa-rouen.fr”. One can get 193.49.10.214 for this machine.

5. Local network
1. arp -a: Ethernet addresses that have been used by your computer. Besides arp displays the contents of a protocol table (MAC, IP addresses).
2. arp -a <IP address in decimal notation>. The same as 5.1, but used for specified host.
3. ping <the same IP address used in 5.2>. We realize that now it appears in arp table, even if it wasn’t there before. Note: Changing arp table is dangerous!
4. ping <broadcast address> Contrarily to 5.3 now it will send packets to all the computers in LAN. 5. So there will be many IP addresses in arp table this time which are added after the command in
    5.4.
6. Yes, the 2 first numbers (192.168.) are the same as they belong to the same LAN. Besides they have common interfaces.

6. Use of traceroute
1. Tracing the route from my station to www2.insa-strasbourg.fr: There are 30 intermediaries.
2. Tracing the route from my station to “www.coria.fr”:
traceroute to www.coria.fr (195.83.86.2), 30 hops max, 60 byte packets
 1 XiaoQiang (192.168.31.1) 7.081 ms 12.653 ms 14.768 ms
 2 * 10.128.36.1 (10.128.36.1) 31.660 ms 34.900 ms
 3 host-149.255.155.133.katv1.net (149.255.155.133) 40.771 ms * 48.198 ms
 4 100.127.1.9 (100.127.1.9) 52.385 ms * *
 5 109.235.198.253 (109.235.198.253) 55.787 ms 59.562 ms *
 6 10.240.0.34 (10.240.0.34) 81.918 ms * 33.723 ms
 7 as57463.0.183.netix.net (193.218.0.183) 174.985 ms 175.867 ms 176.770 ms
 8 renater.equinix-ix.fr (195.42.145.38) 96.853 ms 97.743 ms 98.786 ms
 9 193.51.180.44 (193.51.180.44) 128.719 ms 193.51.180.42 (193.51.180.42) 130.067 ms x	e0-0-1-paris1-rtr-131.noc.renater.fr (193.51.177.10) 135.641 ms
10 te4-2-rouen-rtr-021.noc.renater.fr (193.51.177.31) 119.484 ms 132.045 ms 133.051 ms
11 syrhano-vl3201-te4-3-rouen-rtr-021.noc.renater.fr (193.51.184.129) 133.858 ms
        105.586 ms 106.271 ms
12 coria-s3ser.syrhano.net (193.48.154.174) 93.663 ms 93.870 ms 95.131 ms
13 * * *
14 * * *
15 * * *
16 * * *
17 * * *
18 * * *
19 * * *
20 * * *
21 * * *
22 * * *
23 * * *
24 * * *
25 * * *
26 * * *
27 * * *
28 * * *
29 * * *
30 * * *

3. Tracing the route from my station to “www.club-internet.fr”:
traceroute to www.club-internet.fr (80.125.163.172), 30 hops max, 60 byte packets
1 XiaoQiang (192.168.31.1) 2.235 ms 3.438 ms 8.992 ms
2 10.128.36.1 (10.128.36.1) 178.865 ms 180.219 ms 181.616 ms
3 host-149.255.155.133.katv1.net (149.255.155.133) 182.847 ms 188.091 ms 189.397 ms
4 100.127.1.9 (100.127.1.9) 192.051 ms * *
5 109.235.198.253 (109.235.198.253) 195.497 ms 196.822 ms 203.768 ms
 6 10.240.0.34 (10.240.0.34) 205.830 ms 223.783 ms *
 7 * * *
 8 * * *
 9 * * *
10 * * *
11 * 202.13.6.109.rev.sfr.net (109.6.13.202) 162.831 ms 169.040 ms
    We observe that gates from 7 to 10 hops away. Probably they don’t send ICMP messages.
4. Tracing the route from my station to “www.sfr.fr”:
cbv3-co-4.gaoland.net (80.81.193.201)
5. Tracing the route from my station to “www.free.fr”:
decix.proxad.net (80.81.192.223)
6. Switzerland
7. In traceroute for “dns1.geis.co.jp” we observed:
4.53.212.94 (4.53.212.94) 363.811 ms 365.519 ms ae-1-2.ear1.SanJose3.Level3.net
which means most probably access happens through USA.
8. In traceroute for “travel.mos.ru”: we observed that Russia passes an access by itself.
9. In traceroute for “www.azedunet.az” we observed that Azerbaidjan passes an access by itself.
10. In traceroute for “www.ebeijing.gov.cn”: China gets this access through Russia (83.169.204.50).
11. In traceroute for “www.president.ir”: Iran gets this access through France
      (tic4.gw.opentransit.net)
12. Spain
NOTE: The results in this section could be slightly different than actual answers due to some problems in testing with traceroute.

7. Routing
1. Tested!
2. http://iplookup.flagfox.net/. This site helps to determine the location of servers just writing the hostname or IP address. For ex, typing www.ufaz.az in search box it will point to Netherlands.
3. netstat -h command provides usage (help option) to use it for examining the routing tables.
4.	netstat -r: displays kernel routing tables
Kernel IP routing table
Destination Gateway Genmask Flags MSS Window irtt Iface
default 192.168.35.254 0.0.0.0 UG 0 0 0 enp1s0
link-local * 255.255.0.0 U 0 0 0 enp1s0
192.168.32.0 * 255.255.252.0 U 0 0 0 enp1s0
netstat -i: Display a table of all network interfaces
Kernel Interface table
Iface MTU Met RX-OK RX-ERR RX-DRP RX-OVR TX-OK TX-ERR TX-DRP TX-	OVR Flg
enp1s0 1500 0 344566 0 2 0 65663 0 0 0 BMRU
lo 65536 0 918 0 0 0 918 0 0 0 LRU
netstat -e: display additional information (extend).

7. Use of a “Looking glass”
We took two places one in USA and one in France and made traceroute from one to the other. We observed that the traceroutes are “symmetrical”.

8. Using the DNS
1. nslookup user-Veriton-X2640G. We get:
Server:	127.0.1.1
Address:	127.0.1.1#53

** server can't find user-Veriton-X2640G: SERVFAIL
2.
a. Locally. Type <nslookup www.ufaz.az> in terminal. The result:
Server:	127.0.1.1
Address:	127.0.1.1#53

Name:	www.ufaz.az
Address: 128.199.45.141
   For finding the secondary name server just type <nslookup ufaz.az>. The result:
Server:	127.0.1.1
Address:	127.0.1.1#53

Name:	ufaz.az
Address: 192.168.3.1
Name:	ufaz.az
Address: 128.199.45.141
Name:	ufaz.az
Address: 192.168.3.2
So the second IP address 128.199.45.141 is primary (as it was before), whereas	the other IP addresses are secondary ones.
b. Remote search. It is useful to use the command <nslookup -type=any insa-rouen.fr> which will show a lot of info (like e-mail addresses of managers, do) about the server. As a result we got the following:
Server:	127.0.1.1
Address:	127.0.1.1#53

Non-authoritative answer:
Name:	insa-rouen.fr
Address: 193.49.10.214
insa-rouen.fr	nameserver = regimr.insa-rouen.fr.-- xaliq agakerimov
insa-rouen.fr	nameserver = ns.insa-rouen.fr.
insa-rouen.fr	nameserver = ns.crihan.fr.
insa-rouen.fr
origin = ns.insa-rouen.fr
mail addr = empty.empty
serial = 7849
refresh = 3600
retry = 600
expire = 1209600
minimum = 3600
insa-rouen.fr	mail exchanger = 4 b-mx-insar.relay.syrhano.net.
insa-rouen.fr	mail exchanger = 4 a-mx-insar.relay.syrhano.net.
insa-rouen.fr	text = "MS=2AB7DF322D24ADCF0C0C2A9CFB11BD7ABDF0EC9D"
insa-rouen.fr	text = "v=spf1 include:criann.fr ip4:193.49.10.114 ip4:193.49.10.54	ip4:134.214.182.44 ~all"

Authoritative answers can be found from:
regimr.insa-rouen.fr	internet address = 193.49.10.1
ns.insa-rouen.fr	internet address = 194.254.19.131
ns.crihan.fr	internet address = 195.221.20.10
ns.crihan.fr	has AAAA address 2001:660:7401:201::10
b-mx-insar.relay.syrhano.net	internet address = 193.52.218.39
a-mx-insar.relay.syrhano.net	internet address = 193.52.218.29
where one can find primary (name server of the
INSA Rouen Normandie domain, and the e-mail address of its manager; the
secondary name servers of this domain, and the time limit of their data: the
mail server of this domain (insa-rouen.fr)).

c. Remote search:
    nslookup usa.gov. Address: 54.85.132.205
    nslookup www.usa.gov:
Server:	127.0.1.1
Address:	127.0.1.1#53

Non-authoritative answer:
www.usa.gov	canonical name = d3373zkzjyplpu.cloudfront.net.
Name:	d3373zkzjyplpu.cloudfront.net
Address: 52.222.163.70
Name:	d3373zkzjyplpu.cloudfront.net
Address: 52.222.163.48
Name:	d3373zkzjyplpu.cloudfront.net
Address: 52.222.163.206
Name:	d3373zkzjyplpu.cloudfront.net
Address: 52.222.163.167

   nslookup gouvernement.fr: Address=185.11.125.117
   nslookup www.gouvernement.fr:
Server:	127.0.1.1
Address:	127.0.1.1#53

Non-authoritative answer:
www.gouvernement.fr	canonical name = www.premier-ministre.gouv.fr.
www.premier-ministre.gouv.fr	canonical name =	sni.www.gouvernement.fr.c.footprint.net.
Name:	sni.www.gouvernement.fr.c.footprint.net
Address: 67.27.251.124
Name:	sni.www.gouvernement.fr.c.footprint.net
Address: 8.241.31.252
Name:	sni.www.gouvernement.fr.c.footprint.net
Address: 67.26.3.252

    nslookup gouvernement.nl: Address=195.193.5.236
    nslookup www.gouvernement.fr:
Server:	127.0.1.1
Address:	127.0.1.1#53

Non-authoritative answer:
www.gouvernement.nl	canonical name = gouvernement.nl.
Name:	gouvernement.nl
Address: 195.193.5.236
3. Using the <dig -q *.suffix> one can find answers to a-d.